I modified the Motorola DTMF Keypad microphone to work with the ICOM 706.

Take apart the microphone and disconnect the blue wire and insulate the end and leave it loose. Connect the black wire to where the wire was connected. I use mic gain of 5 working SSB with the ICOM 706.

Okay, I've got a new Icom IC-706MKIIG info for you:

There is a mod saying:

"Push P.AMP/ATT and RIT/SUB while power up and you will be able to see SHIFT-ADJ on your 706mkII. Dont know what this is for, recalibrating ?"

I have tested this and figured out the following:

When the SHIFT knob is in the middle position and you press SHIFT-ADJ, then "Good" is displayed. Nothing happens after power on.

But when you turn the SHIFT knob a little to the left or to the right, then good is displayed and next time you power up you have a modified shift adjustment. The SHIFT graph is different, too!

If you turn the knob a bit more to the left or to the right, then "Error" is displayed and nothing happens.

I wrote to Icom Europe and they say, that this function (P.AMP/ATT + RIT/SUB) is only used in the factory during the production process of the IC-706MKIIG. to calibrate the centersetting of the shift know.

Afterwards a new calibration shouldn't be necessary.

When you press the arrow in the SHIFT-ADJ menu for one second, the position of the shift know is stored as the new center setting.

If you would like to increased recieve on your 706mk2g, here is the procedure.

Take off top cover with front facing you. Behind the left of the VFO against the front of the case is 2 square cans with black phillips screws in them. Don't adjust these, right behind them in the middle is a metal ajustment screw that looks like most of the other ones, like the ajustments for power etc.

Have your radio on SSB and turn clockwise and you will hear the recieve increase. Only turn it a little, that does a lot, you don't want to over do it. Too much will bring in a lot of noise.

I've done it to mine and it really made the ears better than from the factory. As you know, the recieve is great on these rigs, but this improves it more. It takes a jewlers flat head screwdriver, be careful. I'm not responsable if you mess up.

Unlike the 706, the 706MKIIG do not keep its internal blower running in receive mode. So, the radio becomes very hot after half-hour or more of operation, especially in summer.

A small 200 ohms 1 watt 1% metal-film resistor connected in the PA board, between the switched +14v and the blower positive lead will make it run very quietly, dropping the external body temperature of the MKIIG very near to that found in the 706.

The voltage applied by the resistor over the cooler is 4.7 volts and it is sufficient to start and keep it running without any perceptible noise.

Resist to temptation of increase the receive-mode blower speed (reducing the resistor ohmic value) avoiding to transform your radio in a vacuum cleaner...

After this modification, the measured radio body temperature after two hours of receive-only mode was 37 at room temperature of 25 ºC (98.6/77 ºF).

This mod will not alter the transmit behavior of the ventilation system that will remain operating as usual or even better because the 46.5 mA auxiliary current supplied by this resistor will keep the blower drive transistor more cooler.

Another benefit is the reduced frequency drift in the VHF and UHF bands, SSB mode*.

One of the resistor lead is connected to the positive of the blower connector and the other in the RF choke (L613) loop as show in the pictures.

If you want added security, provide some isolation on the resistor leads. DO NOT short circuit the choke winding and be very careful when soldering the resistor lead over the male PC connector pin.

In this mod, there is no necessity of board removal and could be done in a matter of minutes. Only the radio bottom cover must be removed (5 screws).

73, Sergio PY1BEK

From: SM6WXO@SM6JZZ.#SDE.R.SWE.EU

I have tried some special buttons on IC706mkII:

Push TS and DISPLAY while power up and you will see a strange power on check.

Push P.AMP/ATT and RIT/SUB while power up and you will be able to see SHIFT-ADJ on your 706mkII. Dont know what this is for, recalibrating ?

I think that these things even works on the older version of 706, dont know.

73 - Dennis, SM6WXO @ SM6JZZ