IC-706MKIIG to SG-239 Interface

Phil Salas – AD5X

This is the interface I’m using with my IC-706G and SG-239.  The 10K resistor between connector pins 2 and 3 tells the IC-706G that a tuner is connected.  However, rather than use the “tune” button on the IC-706G, I use a separate momentary SPSP pushbutton switch as shown.  This way I don’t have to mess with the big capacitor and a fixed tuning time.

# Text boxes

RS274-224

To IC-706

Pin 1: key

Pin 2: start

Pin 3: +12V

Pin 4: gnd

•

•

10K

To SG-239

+12V

Gnd

IC-706 to SG-239 Interface